## Slide 1
SEMICON INDIA HACKATHON 2026 · IDEA SUBMISSION
SpectraRestore
Fast Restoration of Semiconductor Inspection Images
KLA · TRACK 1 · PS01
AI-BASED IMAGE RESTORATION
TEAM <TEAM NAME> · <COLLEGE NAME>
Member | Role | Branch / Year | Contact
<Member 1> | Team Lead · Model architecture & training | <Branch, Year> | <email / phone>
<Member 2> | Data pipeline & augmentation | <Branch, Year> | <email>
<Member 3> | Evaluation, metrics & benchmarking | <Branch, Year> | <email>
<Member 4> | Repo, documentation & presentation | <Branch, Year> | <email>
Submission: TeamName_KLA_PS01.pdf · GitHub repository linked on Slide 8

## Slide 2
SLIDE 2 · PROBLEM STATEMENT ADDRESSED
AI-Based Restoration of Degraded Images
02 / 09
SEMICON India Hackathon 2026 · KLA Track 1 — AI-Based Restoration of Degraded Images
Why this matters
Inspection tools capture microscopic grayscale images of chip structures to catch defects. A single pixel of noise or one lost detail can hide a defect — and a missed defect is a failed chip.
Today, engineers simply tolerate degraded images. Learned restoration upgrades every inspection tool's image quality in software — better defect detectability with zero new hardware, directly serving yield.
The task
Learn one model: degraded 128² / 256² input → clean 2× output in [0, 1].
Judged on SSIM · pSNR · LPIPS, out-of-distribution robustness, and inference time on an H100 GPU.
KLA's own guidance: degradations “may appear in any order” — so we invert the mapping from pairs instead of modelling the degradation chain.
1 · Speckle noise
Multiplicative grain that pushes pixel values OUTSIDE [0, 1] while ground truth stays in [0, 1] — “a feature, not a bug” per KLA. Must be removed without blurring real structure.
2 · Additive Gaussian noise
Softens edges and washes out fine structure. Sharpness must return without ringing or artificial patterns.
3 · 2× downsampling
512² arrives as 256² (or 256² as 128²). Fine periodic detail is destroyed and must be reconstructed at 2× resolution.

## Slide 3
SLIDE 3 · IDEA DESCRIPTION
One fast network, joint denoise + 2× super-resolution
03 / 09
SEMICON India Hackathon 2026 · KLA Track 1 — AI-Based Restoration of Degraded Images
A single NAFNet-based image-to-image network restores all three degradations in one forward pass — trained with a metric-matched loss (Charbonnier + SSIM + FFT + LPIPS) and degradation augmentation for out-of-distribution robustness.
Joint model, not a pipeline
Denoise-then-upscale propagates errors between stages and doubles latency. One network shares features across denoising and detail reconstruction — faster AND better.
Regression, not generation
No GAN, no diffusion. Generative models hallucinate texture — a hallucinated edge can fake or hide a defect. Regression directly optimises the announced metrics in a single pass.
Compute where it's cheap
All heavy processing runs at LOW input resolution (~4× cheaper than at 2×); upsampling happens only at the very end. This is why the design wins the H100 timing benchmark.
Degradation | How the design handles it
Speckle (out-of-range values) | No input clipping; per-image standardisation absorbs the extended range; residual learning preserves true structure
Gaussian noise | Denoising backbone + SSIM & FFT loss terms restore edge sharpness without ringing
2× resolution loss | PixelShuffle sub-pixel tail reconstructs detail; FFT loss supervises the periodic spectrum

## Slide 4
SLIDE 4 · PROPOSED SOLUTION
Architecture — NAFNet-SR2× and the training recipe
04 / 09
SEMICON India Hackathon 2026 · KLA Track 1 — AI-Based Restoration of Degraded Images
Degraded input
1 × H × W
values may exceed [0,1]
Standardise
per-image
(x − μ) / σ
NAFNet U-Net
enc [2,2,4,8] · mid 12 · dec [2,2,2,2]
width 32 · at input resolution
PixelShuffle ×2
sub-pixel conv
learned upsampling
Restored output
1 × 2H × 2W
clamped to [0,1] at save
+ global residual skip: noisy bilinear-upsampled input (absolute intensity) + learned correction. Input-only standardisation — output stays in GT space (no degraded mean/std re-applied).
Loss — matched to the metrics
1.00 Charbonnier (pSNR proxy) + 0.20 (1−SSIM) + 0.05 FFT-L1 (periodic detail) + 0.10 LPIPS enabled after 20% warm-up (prevents early artifacts). No adversarial loss.
Optimisation
AdamW · LR 3e-4 → cosine to 1e-6 · ~200k iters · bf16 mixed precision · EMA 0.999 (EMA checkpoint ships) · checkpoint chosen by combined val SSIM + pSNR + (1−LPIPS).
Data & augmentation
Held-out val/ split · aligned random crops (128² in / 256² GT) · flips + 90° rotations only · degradation aug: extra speckle / Gaussian / mild blur (p≈0.3).
Inference (what KLA benchmarks)
FP16 + channels_last, single forward pass · ~29.2M params (width 32 default) · measure latency on target GPU · fast (~15M) preset if timing dominates · TTA off by default.

## Slide 5
SLIDE 5 · INNOVATION & UNIQUENESS
What makes this approach different
05 / 09
SEMICON India Hackathon 2026 · KLA Track 1 — AI-Based Restoration of Degraded Images
1 · Degradation augmentation
With p≈0.3 we inject EXTRA randomised speckle, Gaussian, or mild blur into already-degraded inputs (targets unchanged). Aligns with KLA webinar factors and widens the degradation family. Ablate with vs without augmentation. True OOD may also be new structures.
2 · Metric-aligned composite loss
Charbonnier (pSNR proxy) + SSIM + FFT-L1 + LPIPS (after warm-up). These are the metrics we report on slides; H100 quality scoring is not fully specified. FFT term targets periodic semiconductor structure that plain L1 tends to blur.
3 · Input-only standardisation
Per-image standardisation on the INPUT only absorbs out-of-range speckle and source shifts. We do NOT re-apply degraded mean/std to the output — predictions stay in absolute GT space ([0,1]), as required by KLA range notes.
4 · Speed as a design constraint
Attention-free NAFNet backbone, compute at low resolution, FP16 inference. Size presets: default ~29.2M, fast ~15M. Report a measured quality-vs-latency curve. Regression-only so the model cannot hallucinate defects — an argument for metrology judges.

## Slide 6
SLIDE 6 · RESULTS
Restoration quality on the held-out validation split
06 / 09
SEMICON India Hackathon 2026 · KLA Track 1 — AI-Based Restoration of Degraded Images
Metric | Degraded input (baseline) | Ours (restored)
SSIM ↑ | <baseline> | <result>
pSNR (dB) ↑ | <baseline> | <result>
LPIPS ↓ | <baseline> | <result>
Inference (ms/img, FP16) | — | <result>
OOD ablation
Same table computed with vs without degradation augmentation on shifted-noise data — the number that proves generalisation. <fill after training>
Visual evidence — degraded input → our restoration → ground truth (with |error| heat-map)
<image>
Degraded input
<image>
Our restoration
<image>
Ground truth
<image>
|error| map
Include at least one hard case (fine periodic array) and 2–3 zoom levels — confusion-free evidence as the brief demands.

## Slide 7
SLIDE 7 · TECHNOLOGY & FEASIBILITY
Standard, reproducible, student-compute friendly
07 / 09
SEMICON India Hackathon 2026 · KLA Track 1 — AI-Based Restoration of Degraded Images
Item | Choice
Framework | PyTorch 2.x + lpips
Model size | ~29.2M default (w32) · ~15M fast · ~65M large
Training hardware | Single A100 / L4 / T4-class cloud GPU
Training time | ~200k iters (batch sized to GPU; Colab T4: batch 4–8)
Inference | FP16, single pass · report measured ms/image
Data handling | Native range preserved; png / tif / npy
Reproducibility | Fixed seeds · logged configs · pip freeze
Why it's feasible
Everything is standard and free of exotic dependencies. The model is deliberately small enough to train on student compute (Colab Pro / Kaggle), and a working checkpoint appears within hours — leaving time for the OOD ablation and visual assets.
Risk → mitigation
Timing weighted heavily → switch to fast (~15M) preset OOD / blur variants → degradation aug (noise + mild blur) Format surprises → loader auto-detects; verify on real data first Filename scoring → evaluate.py writes same names as inputs

## Slide 8
SLIDE 8 · GITHUB & VIDEO LINK
Repository & demo
08 / 09
SEMICON India Hackathon 2026 · KLA Track 1 — AI-Based Restoration of Degraded Images
GitHub (mandatory): github.com/<org>/<repo>
Demo video (optional): <link — screen capture of evaluate.py restoring the test set>
Repository contents — exactly per the KLA checklist
# | Item | What we ship
1 | README.md | Clone → install → download weights → run inference in ≤5 commands, no contact needed
2 | evaluate.py (standalone) | Takes --input_dir and --output_dir · same output filenames as inputs · auto-loads weights · zero manual edits · fresh-machine tested
3 | train.py | Reproduces the full training run from scratch (config + seeds)
4 | Trained weights | EMA checkpoint (.pt) via Git LFS / Drive / HuggingFace
5 | outputs/ | Actual restored test images produced by our model
6 | requirements.txt | Full pip freeze from the training environment
The evaluation script is the critical file — KLA runs it AS-IS on the H100 to score quality and speed. It is tested on a clean machine before submission.

## Slide 9
SLIDE 9 · REFERENCES
References
09 / 09
SEMICON India Hackathon 2026 · KLA Track 1 — AI-Based Restoration of Degraded Images
1. Chen, L. et al. — Simple Baselines for Image Restoration (NAFNet), ECCV 2022.
2. Shi, W. et al. — Real-Time Single Image and Video Super-Resolution Using an Efficient Sub-Pixel Convolutional Neural Network (PixelShuffle), CVPR 2016.
3. Zhang, R. et al. — The Unreasonable Effectiveness of Deep Features as a Perceptual Metric (LPIPS), CVPR 2018.
4. Zhai, L. et al. — A Comprehensive Review of Deep Learning-Based Real-World Image Restoration, IEEE Access 11, 2023.
5. Kumar, T. et al. — Image Data Augmentation Approaches: A Comprehensive Survey and Future Directions, IEEE Access 12, 2024.
6. Terven, J. et al. — A Comprehensive Survey of Loss Functions and Metrics in Deep Learning, Artificial Intelligence Review 58, 195, 2025.
7. Monga, V. et al. — Algorithm Unrolling: Interpretable, Efficient Deep Learning for Signal and Image Processing, IEEE Signal Processing Magazine 38(2), 2021.
8. Wang, Z. et al. — Image Quality Assessment: From Error Visibility to Structural Similarity (SSIM), IEEE Transactions on Image Processing, 2004.
References 4–7 are the papers cited in KLA's own problem-statement webinar deck — our augmentation and loss choices are justified against them.